Coil Driver Kit
Version 1.2
For batch 2011-03

Board Errata
- Replace 4k Resistor with 3.9k
- BC556 Transistor replaced by BC337
- BC546 Transistor replaced by BC327
- 5A fuse replaced by 10A fuse (5A is notionally safer, but tends to blow unnecessarily)
- Kit is actually licensed under the TAPR NCL not the TAPR OHL
  We have no objection to others selling a version of this kit, we just prefer that they pick up the phone first and would prefer our names not be on something we would consider sub-standard.

Parts List

Qty	Part Description	Package	Distinguishing Features / Marking
1	600v N-Channel IGBT	TO220
1	Signal Transistor BC327	TO92	Bent leads, Marked 'BC 7-25' (Printing Error?)
1	Signal Transistor BC337	TO92	Straight leads, Marked BC337-25
1	12R Resistor		Brown	Red	Black	Gold	Brown
1	68R Resistor		Blue	Grey	Black	Gold	Brown
1	220R Resistor		Red	Red	Black	Black	Brown
1	620R Resistor		Blue	Red	Black	Black	Brown
2	1K2 Resistor		Brown	Red	Black	Brown	Brown
1	2K2 Resistor		Red	Red	Black	Brown	Brown
1	3K9 Resistor		Orange	White	Black	Brown	Brown
2	2R2 Power Resistor	Large Ceramic	Large white resistor printed with '10W 2R2J'
1	10nF Capacitor	MKT
1	63v 1uF Capacitor	Electrolytic
1	16v 4700uF Capacitor	Electrolytic
1	15v Zener Diode	DO-35	Slightly longer than 1N4148
5	75v Zener Diode	017AA
1	Rectifier Diode 1N4148	DO-35	Slightly shorter than 15v Zener
1	50K Cermet Trimpot
1	NE555 Timer IC	DIP-8
1	4N35 Opto-Isolator	DIP-6
2	Fuse Clips
1	10A Fuse
1	2.54mm Shunt
2	2x1 2.54mm Pin Header
1	Red LED	3mm	Diffused Red Lens
1	Blue LED	3mm	Waterclear Lens

Assembly Instructions

Install the components starting with the lowest-profile parts first to aid in keeping things flush when soldering.
You must install the 15v gate protection Zener diode before installing the IGBT to prevent damage from ESD.

Be careful when clipping leads from the resistors as the pads are smaller than they should be and can lift if pulled.

TODO: More Instructions!

Operation Instructions

The coil driver can operate in 2 modes, internal and external oscillator. The internal oscillator is based on a 555 timer using a trim-pot to adjust the output frequency. In external oscillator mode the board will take a 5v TTL signal through a 4N35 opto-isolator.